## Slide 1: Internet of Things: IPV6 Lect #09 - 11
Prof. Suchismita Chinara
Dept. of Computer Science Engg.
National Institute of Technology Rourkela-769008

## Slide 2: IPV6 address format
The prefix describes the public topology that is usually allocated to your site by an ISP or Regional Internet Registry (RIR)
The subnet ID describes the private topology, also known as the site topology
For example in IPV6 address - 2001:0db8:3c4d:0015:0000:0000:1a2f:1a2b
The first 48 bits 2001:0db8:3c4d contain the site prefix, representing the public topology.
The next 16 bits 0015 contain the subnet ID, representing the private topology for the site
The lower order 64 bits 0000:0000:1a2f:1a2b contain the interface ID.

## Slide 3: IPv6 address formats
The size and format of the IPv6 address expand addressing capability.
The IPv6 address size is 128 bits.
Most IPv6 addresses do not occupy all of their possible 128 bits. This condition results in fields that are padded with zeros or contain only zeros
The preferred IPv6 address representation is: x:x:x:x:x:x:x:x,Where each x is the hexadecimal values of the eight 16-bit pieces of the address.
IPv6 addresses range from
0000:0000:0000:0000:0000:0000:0000:0000 to
ffff:ffff:ffff:ffff:ffff:ffff:ffff:ffff

## Slide 4: IPv6 address formats
In addition to this preferred format, IPv6 addresses might be specified in two other shortened formats:
Omit leading zeros
  Specify IPv6 addresses by omitting leading zeros. For example, IPv6 address
  1050:0000:0000:0000:0005:0600:300c:326b can be written as
  1050:0:0:0:5:600:300c:326b
Double colon
  Specify IPv6 addresses by using double colons (::) in place of a series of zeros. For example, IPv6 address
  ff06:0:0:0:0:0:0:c3 can be written as
  ff06::c3. Double colons can be used only once in an IP address

## Slide 5: Prefixes in IPV6
Let the IPV6 address be 2001:db8:3c4d:0015:0000:0000:1a2f:1a2b
with zeros compressed, the site prefix can be 2001:db8:3c4d::/48
The subnet prefix can be represented as 2001:db8:3c4d:15::/64 (The subnet prefix always contains 64 bits. These bits include 48 bits for the site prefix, in addition to 16 bits for the subnet ID)
Special prefixes are:
  2002::/16 - Indicates that a 6 to 4 routing prefix follows
  fe80::/10 – Indicates that a link-local address follows
  ff00::/8 - Indicates that a multicast address follows

## Slide 6: Embedding IPV4 into IPV6
An alternative format for IPv6 addresses combines the colon and dotted notation, so the IPv4 address can be embedded in the IPv6 address.
Hexadecimal values are specified for the left-most 96 bits, and decimal values are specified for the right-most 32 bits indicating the embedded IPv4 address.
This format ensures compatibility between IPv6 nodes and IPv4 nodes when you are working in a mixed network environment.

## Slide 7: Embedding IPV4 into IPV6
IPv4-mapped IPv6 address uses this alternative format.
This type of address is used to represent IPv4 nodes as IPv6 addresses.
It allows IPv6 applications to communicate directly with IPv4 applications.
For example, 0:0:0:0:0:ffff:192.1.56.10 and
  ::ffff:192.1.56.10 are the same.

## Slide 8: IPv6 address types
IPv6 addresses are categorized into these basic types:
Unicast address
Anycast address
Multicast address

## Slide 9: Unicast address
The unicast address specifies a single interface.
A packet sent to a unicast address destination travels from one host to the destination host.
The two regular types of unicast addresses include:
  Link-local address
    Link-local addresses are designed for use on a single local link (local network).
    Link-local addresses are automatically configured on all interfaces.
    The prefix used for a link-local address is fe80::/10.
    Routers do not forward packets with a destination or source address containing a link-local address.
  Global address
    Global addresses are designed for use on any network.
    The prefix used for a global address begins with binary 001

## Slide 10: Unicast Address:
Link Local Unicast Address:
Global Unicast address

## Slide 11: Special unicast address
Unspecified address
  The unspecified address is 0:0:0:0:0:0:0:0.
  You can abbreviate the address with two colons (::).
  The unspecified address indicates the absence of an address, and it can never be assigned to a host.
  It can be used by an IPv6 host that does not yet have an address assigned to it.
  For example, when the host sends a packet to discover if an address is used by another node, the host uses the unspecified address as its source address.
Loopback address
  The loopback address is 0:0:0:0:0:0:0:1.
  You can abbreviate the address as : :1.
  The loopback address is used by a node to send a packet to itself.

## Slide 12: IPV6: Anycast Address
An anycast address specifies a set of interfaces, possibly at different locations, that all share a single address.
A packet sent to an anycast address goes only to the nearest member of the anycast group.

## Slide 13: Anycast Addressing in IPV6
B

## Slide 14: IPV6: Multicast Address
The multicast address specifies a set of interfaces, possibly at multiple locations.
The prefix used for a multicast address is FF.
If a packet is sent to a multicast address, one copy of the packet is delivered to each member of the group.

## Slide 15: IPV6: Neighbour discovery Protocol
Neighbor discovery allows hosts and routers to communicate with one another.
Neighbor discovery functions are used by IPv6 nodes (hosts or routers)
  to discover the presence of other IPv6 nodes,
  to determine the link-layer addresses of nodes,
  to find routers that are capable of forwarding IPv6 packets, and
  to maintain a cache of active IPv6 neighbors.

## Slide 16: IPV6: Neighbour discovery
IPv6 nodes use these five Internet Control Message Protocol version 6 (ICMPv6) messages to communicate with other nodes:
Router solicitation
Router advertisement
Neighbour solicitation
Neighbour advertisement
Redirect

## Slide 17: IPV6: Neighbour discovery
Router solicitation
  Hosts send these messages to request routers to generate router advertisements.
  A host sends an initial router solicitation when the host first becomes available on the network.
Router advertisement
  Routers send these messages either periodically or in response to a router solicitation.
  The information provided by router advertisements is used by hosts to automatically create global interfaces, and associated routes.
  Router advertisements also contain other configuration information used by a host such as MTU and hop limit.

## Slide 18: IPV6: Neighbour discovery
Neighbor solicitation
  Nodes send these messages to determine the link-layer address of a neighbor, or to verify that a neighbor is still reachable.
Neighbor advertisement
  Nodes send these messages in response to a neighbor solicitation or as an unsolicited message to announce an address change.
Redirect
  Routers use these messages to inform hosts of a better first hop for a destination.

## Slide 19: IPV6 Packet
An IPv6 packet is the smallest message entity exchanged using Internet Protocol version 6 (IPv6).
Packets consist of control information for addressing and routing and a payload of user data.
The control information in IPv6 packets is subdivided into a mandatory fixed header and optional extension headers.
The payload of an IPv6 packet is typically a datagram or segment of the higher-level transport layer protocol, but may be data for an internet layer (e.g., ICMPv6) or link layer instead.

## Slide 20: IPV6 Packet
IPv6 packets are typically transmitted over the link layer (i.e., over Ethernet or Wi-Fi), which encapsulates each packet in a frame.
In contrast to IPv4, routers do not fragment IPv6 packets larger than the maximum transmission unit (MTU), it is the sole responsibility of the originating node. A minimum MTU of 1,280 bytes is mandated by IPv6, but hosts are "strongly recommended" to use Path MTU Discovery to take advantage of MTUs greater than the minimum.

## Slide 21: IPv4 vs IPv6 Header

## Slide 22: IPv6 Packet: Fixed header
The fixed header starts an IPv6 packet and has a size of 40 bytes (octets) / (320 bits)

## Slide 23: IPv6 Packet: Fixed header
Version (4 bits)
  The constant 6 (bit sequence 0110)
Traffic Class (6+2 bits)
  The bits of this field hold two values. The six most-significant bits hold the differentiated services field (DS field), which is used to classify packets. This replaces ToS field of IPV4 to let the router know what services should be provided to this packet.
  The remaining two bits are used for Explicit Congestion Notification (ECN); priority values subdivide into ranges: traffic where the source provides congestion control and non-congestion control traffic.

## Slide 24: IPv6 Packet: Fixed header
Flow Label (20 bits)
  This is used to identify the sequence of packets. It helps in prioritizing packet delivery and providing real time service. The vital packets can be delivered ahead of the lower priority packets. The special flow label 0 means the packet does not belong to any flow. Else it identifies flow by source address and port, destination address and port, protocol (value of the last Next Header field).
Payload Length (16 bits)
  The size of the payload in bytes, including any extension headers. This identifies the length of the IPv6 payload (the rest of the packet following the IPV6 header). It is used in place of TLEN of IPv4.

## Slide 25: IPv6 Packet: Fixed header
Next Header (8 bits)
  This is similar to the protocol field in IPv4 header. Specifies the type of the extension header that follows the primary IPv6 header. This field usually specifies the transport layer protocol used by a packet's payload. When extension headers are present in the packet this field indicates which extension header follows.

## Slide 26: Next Header (8 bits)

## Slide 27: Extension Headers (EH) in IPv6 packets

## Slide 28: IPV6 Packet: Fixed header
Hop Limit (8 bits)
  Replaces the time to live field in IPv4. This value is decremented by one at each forwarding node and the packet is discarded if it becomes 0. However, the destination node should process the packet normally even if received with a hop limit of 0.
Source Address (128 bits)
  As in IPv4, this specifies the sender’s IP 128-bit address.
Destination Address (128 bits)
  Similar to IPv4, the destination’s IP address is denoted here.

## Slide 29: IPv6 Extension Header

## Slide 30: Extension Headers (EH) in IPv6 packets

## Slide 31: Extension Headers (EH) in IPv6 packets
In order to rectify the limitations of the IPv4 Option Field, Extension Headers are introduced in IP version 6.
The next Header field of IPv6 fixed header points to the first Extension Header and this first extension header points to the second extension header and so on.
The IPv6 header consists of a 40-byte header followed by up to six optional extension headers

## Slide 32: Extension Headers (EH) in IPv6 packets

## Slide 33: IPV6: Extension Header (EH)
Extension headers (EH) carry optional internet layer information and are placed between the fixed header and the upper-layer protocol header.
Extension headers form a chain, using the Next Header fields.
The Next Header field in the fixed header indicates the type of the first extension header; the Next Header field of the last extension header indicates the type of the upper-layer protocol header in the payload of the packet.

## Slide 34: IPV6: Extension Headers and Their Recommended Order in a Packet
IPv6 packet may contain zero, one or more extension headers but these should be present in their recommended order:

## Slide 35: IPv6: Extension Header
There are several extension headers defined, and new extension headers may be defined in the future.
Most extension headers are examined and processed at the packet's destination.
Hop-by-Hop Options can be processed and modified by intermediate nodes and, if present, must be the first extension.
All extension headers are optional and should only appear at most once, except for the Destination Options header extension, which may appear twice.

## Slide 36: EHs of IPv6

## Slide 37: IPV6: Extension Header
Value 59 (No Next Header) in the Next Header field indicates that there is no next header whatsoever following this one, not even a header of an upper-layer protocol.
It means that, from the header's point of view, the IPv6 packet ends right after it: the payload should be empty.
There could, still be data in the payload if the payload length in the first header of the packet is greater than the length of all extension headers in the packet.
This data should be ignored by hosts, but passed unaltered by routers.

## Slide 38: IPV6 Extension Header: Hop-by-hop options
The Hop-by-Hop Options extension header may be examined and altered by all nodes on the packet's path, including sending and receiving nodes.

## Slide 39: IPV6 Extension Header: Destination options
The Destination Options extension header needs to be examined by the destination node(s) only.
The possible use of this header, intended only for the destination, has not been defined so far.

## Slide 40: IPV6: Extension Header: Routing
The Routing extension header is used to direct a packet to one or more intermediate nodes before being sent to its destination.
Specifies a set of routers that the datagram must visit.

## Slide 41: IPV6 Extension Header: Fragment
In IPv6, the routers do not fragment packets. When a packet is too long for a router to handle, the router sends an ICMP message to the source asking it to fragment the packet and resend it.
In order to send a packet that is larger than the path MTU, the sending node splits the packet into fragments.
This header specifies which fragment of a larger packet this IPv6 packet contains. By using this extension header, the destination can reassemble the packet as in IPv4.

## Slide 42: IPV6 Extension Header: Fragment

## Slide 43: IPV6 Extension Header: Fragment
Next header (8 bits)
  Identifies the type of the next header.
Reserved (8 bits)
  Initialized to all zeroes.
Fragment offset (13 bits)
  Offset, in 8-octet units, relative to the start of the fragmentable part of the original packet.
Res (2 bits)
  Reserved; initialized to zeroes.
M Flag (1 bit)
  1 means more fragments follow; 0 means last fragment.
Identification (32 bits)
  Packet identification value, generated by the source node. Needed for reassembly of the original packet.

## Slide 44: Example of Next Headers (Fragmentation)

## Slide 45: IPV6 Extension Header: Authentication
This header contains a checksum that enables the destination to authenticate the sender.

## Slide 46: IPV6 Extension Header: Encapsulating Security Payload
This header contains the encryption key number and the encrypted payload.
The destination can recover the original payload from these two items using a decryption algorithm that is left to the choice of the user.