## Slide 1: Internet of Things Lect. # 3 -6
Prof. Suchismita Chinara
Dept. of Computer Science Engg.
National Institute of Technology Rourkela-769008

## Slide 2: IoT Level 1
This level consists of data collection, analysis, control & monitoring app. • The data sensed is stored locally. • The data analysis is done locally. • Monitoring & Control is done using Mobile app or web app. • The data generated in this level application is not huge. • All the control actions are performed through internet.
Example: Room temperature is monitored using temperature sensor and data is stored/analysed locally. Based on analysis made, control action is triggered using mobile app or it can just help in status monitoring.

## Slide 3: Level – 1 IoT

## Slide 4: IoT Level 2
This level consists of Big data (Bigger than level -1, data analysis done here) , cloud, control & monitoring app. • This level-2 is complex compared to level-1as rate of sensing is faster. • This level has voluminous size of data. Hence cloud storage is used. • Data analysis is carried out locally. Cloud is used for only storage purpose. • Based on data analysis, control action is triggered using web app or mobile app.
• Examples: In Level 2 IoT, the sensor reads the room temp at better pace and rate than Level 1, data goes to cloud for storage, analysis done locally, action triggered thru the mobile app.

## Slide 5: Level -2 IoT

## Slide 6: IoT Level 3
This level consists of big data collection (Bigger than level-1) , cloud (for data analysis), and control & monitoring app. • Data here is voluminous i.e. big data. Frequency of data sensing is fast and collected sensed data is stored on cloud as it is big. • Data analysis is done on the cloud side and based on analysis control action is triggered using mobile app or web app.
• Examples: Agriculture applications, where analysis of data occurs in the cloud.

## Slide 7: Level 3 IoT

## Slide 8: IoT Level 4
This level consists of multiple sensors, data collection, analysis, and control & monitoring app. • At this level-4, multiple sensors are used which are independent of each other. • The data collected using these sensors are uploaded to the cloud separately. The cloud storage is used in this level due to requirement of huge data storage. • The data analysis is performed on the cloud and based on which control action is triggered either using web app or mobile app.

## Slide 9: Level 4 IoT

## Slide 10: IoT Level 5
This level consists of multiple sensors, coordinator node, data collection, analysis, and control & monitoring app. • This level is similar to level-4 which also has huge data and hence they are sensed using multiple sensors at much faster rate and simultaneously. • The data collection and data analysis is performed at the cloud level. • Based on analysis, control action is performed using mobile app or web app.

## Slide 11: Level 5 IoT

## Slide 12: Introduction to Microcontrollers

## Slide 13: Microcontrollers
Evolution of Microcontrollers
  8051
  80151
  80251
  MCS96
  LPC2148

## Slide 14: Microcontroller
A microcontroller is a small and low-cost computer, which is designed to perform the specific tasks of embedded systems.
The general microcontroller consists of the processor, the memory (RAM, ROM, EPROM), Serial ports, peripherals (timers, counters), etc.
It is built with CMOS technology, which requires less power to operate.
It consists of CPU, RAM, ROM, I/O ports.

## Slide 15: Types of Microcontrollers
Microcontrollers are divided into various categories based on:
  memory
  architecture
  bits
  instruction sets.

## Slide 16: Types based on Bit configuration
8-bit microcontroller − This type of microcontroller is used to execute arithmetic and logical operations like addition, subtraction, multiplication division, etc. For example, Intel 8031 and 8051 are 8 bits microcontroller. (Arduino Uno is 8 bit )
16-bit microcontroller − This type of microcontroller is used to perform arithmetic and logical operations where higher accuracy and performance is required. For example, Intel 8096 is a 16-bit microcontroller.
32-bit microcontroller − This type of microcontroller is generally used in automatically controlled appliances like automatic operational machines, medical appliances, etc. (ESP32, Raspberry pi pico)

## Slide 17: Types based on memory configuration
External memory microcontroller − This type of microcontroller is designed in such a way that they do not have a program memory on the chip. Hence, it is named as external memory microcontroller. For example: Intel 8031 microcontroller.
Embedded memory microcontroller − This type of microcontroller is designed in such a way that the microcontroller has all program and data memory, counters and timers, interrupts, I/O ports are embedded on the chip. For example: Intel 8051 microcontroller.

## Slide 18: Types based on Instruction sets
CISC − CISC stands for Complex Instruction Set Computer. It allows the user to insert a single instruction as an alternative to many simple instructions.
RISC − RISC stands for Reduced Instruction Set Computers. It reduces the operational time by shortening the clock cycle per instruction.

## Slide 19: 8051 Microcontroller Architectural Layout

## Slide 20: 8051 Microcontroller Architectural Layout

## Slide 21: 8051 Microcontroller : Features supported
8-bit microcontroller supporting 8-bit operations.
Many general purpose (GPR) and few special function registers (SFRs)
  Two major 8-bit registers for arithmetical operations - A and B. A is the accumulator register and it is a bit addressable register
  21 SFRs.
  Few registers are bit addressable.
  Control registers for timer, serial communication, and interrupts fall under SFR category.

## Slide 22: 8051 Microcontroller : Features supported
Four register banks having 8 registers in each bank.
  These 32 registers can be used by the programmers
  Stack pointer register: points to the stack (8-bit register)
Data pointer (DPTR): 16 bit register (combination of two 8-bit registers (DPL & DPH)
16-bit program counter (PC) – holds the address of the next instruction to be executed.
8- bit Program Status Word (PSW) – It is the flag register and helps in selection of register banks as well.

## Slide 23: Program Status Word (PSW)

## Slide 24: PSW

## Slide 25: PSW

## Slide 26: 8051 Microcontroller : Features supported
Internal ROM or EPROM: size 4K
Internal user accessible RAM 128 bytes
40 pins package: four ports P0, P1, P2, and P3 ( can be configured as input or output ports)
Two 16 bits timer / counter: T0 and T1
Full duplex serial data receiver / transmitter
Support for interrupt programming
Oscillator and clock circuit
Easier and simpler instruction set

## Slide 27: 8051 pin description

## Slide 28: 8051 pin description
Pins 1 to 8 − These pins are known as Port 1. This port doesn’t serve any other functions. It is internally pulled up, bi-directional I/O port.
Pin 9 − It is a RESET pin, which is used to reset the microcontroller to its initial values.
Pins 10 to 17 − These pins are known as Port 3. This port serves some functions like interrupts, timer input, control signals, serial communication signals RxD and TxD, etc.
Pins 18 & 19 − These pins are used for interfacing an external crystal to get the system clock.
Pin 20 − This pin provides the power supply to the circuit.
Pins 21 to 28 − These pins are known as Port 2. It serves as I/O port. Higher order address bus signals are also multiplexed using this port.
Pin 29 − This is PSEN pin which stands for Program Store Enable. It is used to read a signal from the external program memory.
Pin 30 − This is EA pin which stands for External Access input. It is used to enable/disable the external memory interfacing.
Pin 31 − This is ALE pin which stands for Address Latch Enable. It is used to demultiplex the address-data signal of port.
Pins 32 to 39 − These pins are known as Port 0. It serves as I/O port. Lower order address and data bus signals are multiplexed using this port.
Pin 40 − This pin is used to provide power supply to the circuit.

## Slide 29: 8051 Memory Organization of Microcontroller
The 8051 microcontroller uses a Harvard architecture, meaning it separates program memory (ROM) and data memory (RAM) into distinct physical spaces.
This separation allows the CPU to fetch instructions and read or write data at the same time, giving the system clear functional roles.
There are two broad categories of memory
  Program Memory
  Data Memory

## Slide 30: Program Memory (ROM)
Permanent storage: Keeps the application code and fixed constants safe even when the power turns off.
Read-only access: The CPU only reads from this space during operation; it cannot write new code to it during normal execution.
Capacity limits: Typically includes 4 KB of internal ROM, expandable up to 64 KB using external chips.

## Slide 31: 8051 Program Memory
Program memory is normally referred as ROM. (non-volatile)
It is accessed through EA pin
If EA is high, internal program memory is accessed from 0000H to 0FFFH memory location and external program memory accessed from 1000H to FFFFH memory locations.
If EA is low, only external program memory accessed from 0000H to FFFFH memory locations.
8051 has a 4K byte internal program memory available

## Slide 32: Access the Program memory
EA = 1 :
The microcontroller executes code from its internal ROM (first 4KB for standard 8051).
If the program counter address goes beyond the internal ROM limit (exceeds 4KB), it automatically shifts to fetch remaining instructions from external memory.
EA = 0 :
The microcontroller ignores all internal ROM entirely.
It fetches all program code from external ROM starting from address 0000H.

## Slide 33: 8051 Program Memory

## Slide 34: 8051 Data memory
Temporary storage: Holds dynamic variables, working data, and intermediate calculation results that change while the program runs.
Read-write access: The CPU can change, update, and clear values in this space instantly.
Structure and layout: Features 128 bytes of internal RAM split into register banks, a bit-addressable area, and general storage, plus Special Function Registers (SFRs). It can also expand up to 64 KB externally.
Volatility: Clears all stored contents completely when the device loses power.
Data memory is of two types
  Internal
  External.

## Slide 35: 8051 Internal Data Memory
The internal data memory consists of
256 bytes, these are divided into
two parts:
00H-7FH for internal data RAM
(128 bytes)
80H-FFH for special function
registers (128 bytes)

## Slide 36: 8051 Internal Data Memory Organization

## Slide 37: 8051 – Register Banks

## Slide 38: 8051 Internal Data Memory Organization
8051 Provides four register bank, but only one register bank can be used at any point in time.
To select the register bank, two bits of PSW (Program Status Word) are used.
From 20H to 2FH (16 bytes or 128 bits) can be used as bit addressable RAM.
The remaining locations (30H to 7EH) of the RAM can be used to store variable data and stack.

## Slide 39: Bit addressable area

## Slide 40: 8051 External Data Memory
8051 has a limited amount of internal memory, so it is possible to extend the memory capacity by interfacing it with external memory devices.
The 8051 gives the facility to interface external RAM and ROM.
This allows the microcontroller to execute larger and more complex programs, store more data, and perform more complex operations.
External memory interfacing typically involves connecting the memory devices to the microcontroller through a data bus and an address bus.
The data bus is used to transfer data between the microcontroller and the memory device, while the address bus is used to select a specific memory location in the memory device.
To interface with external memory, the 8051 microcontroller uses dedicated pins such as ALE (Address Latch Enable), PSEN (Program Store Enable), and RD (Read) and WR (Write) signals.
These signals are used to control the flow of data between the microcontroller and the external memory device.

## Slide 41: Why need External Memory Interfacing in 8051 Microcontroller ?
Limited internal memory: The 8051 microcontroller has a limited amount of internal memory, including 128 bytes of RAM and 4KB of on-chip ROM. This memory may not be sufficient for some applications that require larger program memory or more data storage.
Larger programs: For applications that require larger programs, such as complex algorithms or multiple functions, external memory interfacing can provide the necessary program memory space to store these programs.
Data storage: Applications that require the storage of large amounts of data, such as data logging or data analysis, may require external memory interfacing to store the data.
Flexibility: External memory interfacing provides greater flexibility in the design of embedded systems, allowing for customization and adaptability to meet specific application requirements.
Cost-effective: External memory devices such as RAM and ROM are relatively inexpensive, making it cost-effective to interface them with the microcontroller instead of using more expensive on-chip memory.

## Slide 42: Introduction to Arduino Uno
Arduino is a tool for making computers that can sense and control more of the physical world than normal desktops.
Its an open source physical computing platform based on a simple microcontroller board and a development environment for writing software for the board.
Arduino can be used to develop interactive objects, taking inputs from sensors, and controlling varieties of lights, and other physical outputs.

## Slide 43: Arduino Uno
To program the ATmega328P microcontroller a serial communicator is required. Serial communication is significant interface between microcontroller and computer.
Arduino UNO has all the necessary Ics for communication. It is build compact into a PCB which has connectors for fast and easy prototyping.

## Slide 44: Components of Arduino Uno
Microcontroller ATmega328
Operating voltage 5v
Input voltage: 7 -12 V
Digital I/O pins 14
Analog input pins 6
DC current per I/O Pin 40mA
DC current for 3.3v pin 50mA
Flash memory 32KB
SRAM 2 KB
EEPROM 1KB
Clock speed 16MHz

## Slide 45: PIN configuration of Arduino Uno

## Slide 46: PIN configuration of Arduino Uno
Vin: This is the input voltage pin of the Arduino board used to provide input supply from an external power source.
5V: This pin of the Arduino board is used as a regulated power supply voltage and it is used to give supply to the board as well as onboard components.
3.3V: This pin of the board is used to provide a supply of 3.3V which is generated from a voltage regulator on the board
GND: This pin of the board is used to ground the Arduino board.
Reset: This pin of the board is used to reset the microcontroller.
Analog Pins: The pins A0 to A5 are used as an analog input and it is in the range of 0-5V.
Digital Pins: The pins 0 to 13 are used as a digital input or output for the Arduino board.
Serial Pins: These pins are also known as a UART pin. It is used for communication between the Arduino board and a computer or other devices. The transmitter pin number 1 and receiver pin number 0 is used to transmit and receive the data resp.
External Interrupt Pins: This pin of the Arduino board is used to produce the External interrupt and it is done by pin numbers 2 and 3.

## Slide 47: PIN configuration of Arduino Uno
PWM Pins: This pins of the board is used to convert the digital signal into an analog by varying the width of the Pulse. The pin numbers 3,5,6,9,10 and 11 are used as a PWM pin.
SPI Pins: This is the Serial Peripheral Interface pin, it is used to maintain SPI communication with the help of the SPI library. SPI pins include:
SS: Pin number 10 is used as a Slave Select
MOSI: Pin number 11 is used as a Master Out Slave In
MISO: Pin number 12 is used as a Master In Slave Out
SCK: Pin number 13 is used as a Serial Clock
LED Pin: The board has an inbuilt LED using digital pin-13. The LED glows only when the digital pin becomes high.
AREF Pin: This is an analog reference pin of the Arduino board. It is used to provide a reference voltage from an external power supply.