## Slide 1: Internet of Things Lect #02
Prof. Suchismita Chinara
Dept. of Computer Science Engg.
National Institute of Technology Rourkela-769008

## Slide 2: IoT Protocol Stack Layers

## Slide 3: Layer 1: Physical or Sensor Layer
This layer is concerned about the physical components, mainly includes sensors.
This layer is responsible for data collection ( mostly sensing).
Choosing the appropriate sensor is the major challenge, as many sensors are available that can do the same task but at different cost.
Ex: temp sensor, humidity sensor etc. are major components for this layer. For industrial automation (IIoT) PLC, actuators are the major components of layer 1.

## Slide 4: Example of Layer 1 devices

## Slide 5: Layer 2 : Processing and Control action layer
This layer comprises of core components like microcontrollers or processors.
The data is received by the microcontrollers from the sensors.
Example microcontrollers are: Arduino, NodeMCU, ESP, ARM etc.
Operating systems, Android, IOS, Linux play a major role to execute the task.
The data collected from the sensors is processed in this layer.
To determine if the data is meaningful a microcontroller should be present.

## Slide 6: Examples
Microcontrollers:
  ARM/ INTEL boards
DEV kits:
  Arduino, Raspberry
OS:
  RTOS, Linux, Android, IoS
Arduino Uno
Raspberry pi

## Slide 7: Layer 3: Hardware interface layer
This layer include components or interfaces used for communication such as RS232, RS485, SPI (Serial Peripheral Interface), I2C (Inter- integrated Circuit), CAN, SCI etc.
These interfaces are used for serial or parallel communication at various baud rates in synchronous/asynchronous modes.
The above mentioned interface protocols ensure flawless communication.

## Slide 8: HW Interface Layer
Components for communication:
Serial / Parallel standards, RS 232, USB, I2C, SPI, CAN, routers etc.
Layer responsible for handshake

## Slide 9: Layer 4: RF Layer
This radio frequency layer houses RF technologies based on short range or long range and data rate desired by the application of use.
The common indoor RF/wireless technologies include Wifi, Bluetooth, Zigbee, NFC, RFID etc.
The common outdoor RF cellular technologies include GSM/GPRS, CDMA, NB-IoT, 5G etc.
RF layer does communication of data using radio frequency based EM waves.
There is another technology which uses light waves for data communication is LiFi.

## Slide 10: Example: RF Layer
Short Range: Low bandwidth, High bandwidth
Long Range: Low bandwidth, High bandwidth
BLE
Wi-Fi

## Slide 11: Layer 5: Session / Message Layer
This layer deals with various messaging protocols such as MQTT, CoAP, HTTP, FTP (or Secured FTP), SSH etc.
It defines how messages are broadcasted to the cloud.
Example Protocols: MQTT, CoAP, HTTP, FTP, SSH
Content: Messaging

## Slide 12: Layer 5: User experience layer
This layer deals with providing best experience to the end users of IoT products.
This layer takes care of rich UI designs with lots of features.
Various languages and tools are developed for the design of GUI interface software.
These include object oriented and procedure oriented technologies as well database languages (DBMS, SQL) in addition to analytics tools.
Technologies: Object oriented, Procedure Oriented
DBMS , SQL: Analytics Tools / Software from vendors

## Slide 13: Layer 7: Application Layer
This layer talks about the possible applications that can be built with the support of the rest of the layers.
It can range from a simple automation application to smart city application.
Example: Smart home, smart city, smart parking, smart energy, smart retail etc.

## Slide 14: IoT Enabling Technologies
Technologies that help in acquiring / sensing data
Technologies that help in analyzing / processing data
Technologies that help in taking control action (Embedded technology)
Technologies that help in enhancing security / privacy

## Slide 15: Sensors
Sensors sense the environment and retrieve data.
They are the starting point in any IoT application.
Ex: for a temperature monitoring application, the temperature sensor fetches data for us to operate on.
Sensors could be analog or digital.
Digital Sensor: LED, Push button switches etc.
Analog Sensor: Pressure, Temperature etc.

## Slide 16: Sensors
A sensor converts the physical action to be measured into an electrical equivalent and processes it so that the electrical signals can be easily sent and further processed.
A sensor consists of three main components:
  (1) The sensing section contains the sensor itself which is based on a particular technology.
  (2) The processing circuitry converts the physical variable into an electrical variable.
  (3) The signal output contains the electronics connected to a control system.

## Slide 17: Sensors
Vibration sensor
Moisture sensor
Temp sensor
Camera
OBD: ELM327
PIR sensor
PH sensor
Pressure, Temp, humidity sensor

## Slide 18: Computing / Storage
Computing is a significant technology in IoT.
As data storage plays a major role in IoT, cloud has grown much more popular as it serves as an affordable, effective and efficient medium for data storage.
Different popular cloud services are:
  IaaS (Infrastructure as a Service) (AWS, Ms Azure)
  PaaS (Platform as a Service)
  SaaS (Software as a Service)

## Slide 19: Embedded Computing Boards
It brings IoT design to reality.
Most of the computing boards available in market are driven by microcontrollers or processors.
Example computing boards are:
  Raspberry Pi
  Arduino
  Node MCU

## Slide 20: Example computing boards
Node MCU Arduino Uno Raspberry Pi 4

## Slide 21: Communication Protocols
Data exchange is possible because of the protocols.
Protocols take care of the following:
  Addressing
  Format of the message
  Message security (encryption & decryption)
  Routing
  Flow control
  Error monitoring
  Sequencing
  Retransmission guidelines
  Segmentation of the data packet

## Slide 22: Embedded Systems
An embedded system is a computer hardware and software embedded together to perform specific tasks.
Key components of an embedded system include microprocessor or microcontroller, memory, networking units, I/O units, and storage.
Embedded systems run embedded operating systems such as real-time systems (RTOS).
Embedded systems range from low-cost miniaturize devices such as digital watches to cameras, vending machines, appliances etc.