## Slide 1: Internet of Things: Addressing & Identification Lect. # 7
Prof. Suchismita Chinara
Dept. of Computer Science Engg.
National Institute of Technology Rourkela-769008

## Slide 2: IPV4 addressing
IPv4 address is divided into two parts:
  Network ID (Identifies a network in the internet)
  Host ID (Identifies the host in a network)
Length of NID and HID are variable

## Slide 3: Special Addresses
Network address
  Netid. Hostid ( All 0’s)
  Ex: Class A: X.0.0.0 (Ex: 44.0.0.0)
  Class B: X.Y. 0.0 (Ex: 130.55.0.0)
  Class C: X.Y.Z.0 (Ex: 192.168.40.0) 192.168.40.1 ----- 192.168.40.254
Direct broadcast address
  Netid. Hostid ( All 1’s)
  Ex: Class A: X.255.255.255
  Class B: X.Y. 255.255
  Class C: X.Y.Z.255

## Slide 4: Special addresses
This host on this network
  Used as a source address (during bootstrap)
  Ex: 0.0.0.0
Specific host on this network
  NetID remains same
  The data does not go through the router
  Src and Dest remains in the same network
  Ex: src 144.14.x.y sends packet to dest 144.14.p.q
Loop back address
  Local Loopback Address is used to let a system send a message to itself to make sure that TCP/IP stack is installed correctly on the machine.
  Typically 127.0.0.1 is used as the local loopback address.

## Slide 5: IPV4 Packet header
Length of IP Header – 20 bytes – 60 bytes (40 bytes optional)

## Slide 6: IP Header Format

## Slide 7: IP Header details
Version − Version no. of Internet Protocol used (e.g. IPv4).
IHL − Internet Header Length HLEN; Length of entire IP header.
Ex: for 20 bytes IP header HLEN= 0101
ToS – Type of Service – 03 bits (precedence fm 000 to 111) – 04 bits (DTRC) – 01 bit (reserved)
  D : Delay to be minimized
  T: Throughput to be maximized
  R: Reliability to be maximized
  C: Cost to be minimized
Total Length − Length of entire IP Packet (including IP header and IP Payload). Data = TLEN - HLEN

## Slide 8
Identification − If IP packet is fragmented during the transmission, all the fragments contain same identification number. to identify original IP packet they belong to.
Flags − As required by the network resources, if IP Packet is too large to handle, these ‘flags’ tells if they can be fragmented or not. In this 3-bit flag, the MSB is always set to ‘0’.
  D – Do not fragment
  M – More fragment
Fragment Offset − This offset tells the exact position of the fragment in the original IP Packet.

## Slide 9
Time to Live − To avoid looping in the network, every packet is sent with some TTL value set, which tells the network how many routers (hops) this packet can cross. At each hop, its value is decremented by one and when the value reaches zero, the packet is discarded.
Protocol − Tells the Network layer at the destination host, to which Protocol this packet belongs to, i.e. the next level Protocol. For example protocol number of ICMP is 1, TCP is 6 and UDP is 17.
Header Checksum − This field is used to keep checksum value of entire header which is then used to check if the packet is received error-free.
Source Address − 32-bit address of the Sender (or source) of the packet.
Destination Address − 32-bit address of the Receiver (or destination) of the packet.
Options − This is optional field, which is used if the value of IHL is greater than 5. These options may contain values for options such as Security, Record Route, Time Stamp, etc.

## Slide 10: IP Fragments & Reassembly